## Slide 1: Logic Design of Asynchronous Circuits
Jordi Cortadella Jim Garside
Alex Yakovlev
Univ. Politècnica de Catalunya, Barcelona, Spain
Manchester University, UK
University of Newcastle upon Tyne, UK

## Slide 2: Outline
I: Basic concepts on asynchronous circuit design
II: Logic synthesis from concurrent specifications
III: Advanced topics on synthesis
IV: Design practice

## Slide 3: Logic Design of Asynchronous Circuits
Part I:
Basic concepts on asynchronous circuit design

## Slide 4: Outline
What is an asynchronous circuit ?
Asynchronous communication
Async Design Styles (Micropipelines, …)
Asynchronous logic building blocks
Control specification and implementation
Delay models and classes of async circuits
Why asynchronous circuits ?

## Slide 5: Synchronous circuit
Implicit (global) synchronization between blocks
Clock Period > Max Delay (CL)
R
R
R
R
CL
CL
CL
CLK

## Slide 6: Asynchronous circuit
R
R
R
R
CL
CL
CL
Explicit (Local) synchronization: Req/Ack handshakes
Req
Ack

## Slide 7: Motivation for asynchronous
Asynchronous design is often unavoidable:
  Asynchronous interfaces, arbiters etc.
Modern clocking is multi-phase and distributed – and virtually ‘asynchronous’ (cf. GALS – next slide):
  Mesachronous (clock travels together with data)
  Local (possibly stretchable) clock generation
Robust asynchronous design flow is coming (e.g. VLSI programming from Philips, Balsa from Univ of Manchester, NCL from Theseus Logic …)

## Slide 8: Globally Async Locally Sync (GALS)
Local CLK
R
R
CL
Async-to-sync Wrapper
Req1
Req2
Req3
Req4
Ack3
Ack4
Ack2
Ack1
Asynchronous World
Clocked Domain

## Slide 9: Key Design Differences
Synchronous logic design:
  proceeds without taking timing correctness (hazards, signal ack-ing etc.) into account
  Combinational logic and memory latches (registers) are built separately
  Static timing analysis of CL is sufficient to determine the Max Delay (clock period)
  Fixed set-up and hold conditions for latches

## Slide 10: Key Design Differences
Asynchronous logic design:
  Must ensure hazard-freedom, signal ack-ing, local timing constraints
  Combinational logic and memory latches (registers) are often mixed in “complex gates”
  Dynamic timing analysis of logic is needed to determine relative delays between paths
To avoid complex issues, circuits may be built as Delay-insensitive and/or Speed-independent (as discussed later)

## Slide 11: Verification and Testing Differences
Synchronous logic verification and testing:
  Only functional correctness aspect is verified and tested
  Testing can be done with standard ATE and at low speed
Asynchronous logic verification and testing:
  In addition to functional correctness, temporal aspect is crucial: e.g. causality and order, deadlock-freedom
  Testing must cover faults in complex gates (logic+memory) and must proceed at normal operation rate
  Delay fault testing may be needed

## Slide 12: Synchronous communication
Clock edges determine the time instants where data must be sampled
Data wires may glitch between clock edges (set-up/hold times must be satisfied)
Data are transmitted at a fixed rate (clock frequency)
1
1
0
0
1
0

## Slide 13: Dual rail
Two wires with L(low) and H (high) per bit
  “LL” = “spacer”, “LH” = “0”, “HL” = “1”
n-bit data communication requires 2n wires
Each bit is self-timed
Other delay-insensitive codes exist (e.g. k-of-n) and event-based signalling (choice criteria: pin and power efficiency)
1
1
0
0
1
0

## Slide 14: Bundled data
Validity signal
  Similar to an aperiodic local clock
n-bit data communication requires n+1 wires
Data wires may glitch when no valid
Signaling protocols
  level sensitive (latch)
  transition sensitive (register): 2-phase / 4-phase
1
1
0
0
1
0

## Slide 15: Example: memory read cycle
Transition signaling, 4-phase
Valid address
Address
Valid data
Data
A
A
D
D

## Slide 16: Example: memory read cycle
Transition signaling, 2-phase
Valid address
Address
Valid data
Data
A
A
D
D

## Slide 17: Asynchronous modules
Signaling protocol:
reqin+ start+ [computation] done+ reqout+ ackout+ ackin+ reqin- start- [reset] done- reqout- ackout- ackin- (more concurrency is also possible)
Data IN
Data OUT
req in
req out
ack in
ack out
DATA
PATH
CONTROL
start
done

## Slide 18: Asynchronous latches: C element
C
A
B
Z
A B Z+
0 0 0
0 1 Z
1 0 Z
1 1 1
Vdd
Gnd
A
A
A
A
B
B
B
B
Z
Z
Z
[van Berkel 91]
Static Logic Implementation

## Slide 19: C-element: Other implementations
A
A
B
B
Gnd
Vdd
Z
A
A
B
B
Gnd
Vdd
Z
Weak inverter
Quasi-Static
Dynamic

## Slide 20: Dual-rail logic
A.t
A.f
B.t
B.f
C.t
C.f
Dual-rail AND gate
Valid behavior for monotonic environment

## Slide 21: Completion detection
Dual-rail
logic
•
•
•
•
•
•
C
done
Completion detection tree

## Slide 22: Differential cascode voltage switch logic
start
start
A.t
B.t
C.t
A.f
B.f
C.f
Z.t
Z.f
done
3-input AND/NAND gate
N-type transistor network

## Slide 23: Examples of dual-rail design
Asynchronous dual-rail ripple-carry adder (A. Martin, 1991)
  Critical delay is proportional to logN (N=number of bits)
  32-bit adder delay (1.6m MOSIS CMOS): 11ns versus 40 ns for synchronous
  Async cell transistor count = 34 versus synchronous = 28
More recent success stories (modularity and automatic synthesis) of dual-rail logic from Null-Convension Logic from Theseus Logic

## Slide 24: Bundled-data logic blocks
Single-rail logic
•
•
•
•
•
•
delay
start
done
Conventional logic + matched delay

## Slide 25: Mutual exclusion element
req1
req2
ack1
ack2
(0)
(0)
(1)
(1)
(0)
(0)
Basic arbitration element: Mutex
An asynchronous data latch with MS resolver can be built similarly
Metastability resolver

## Slide 26: Micropipelines (Sutherland 89)
C
Join
Merge
Toggle
r1
r2
g1
g2
d1
d2
Request-Grant-Done (RGD)Arbiter
Call
r1
r2
r
a
a1
a2
Select
in
outf
outt
sel
in
out0
out1
Micropipeline (2-phase) control blocks

## Slide 27: Micropipelines (Sutherland 89)
L
L
L
L
logic
logic
logic
Rin
Aout
C
C
C
C
Rout
Ain
delay
delay
delay

## Slide 28: Data-path / Control
L
L
L
L
logic
logic
logic
Rin
Rout
CONTROL
Ain
Aout

## Slide 29: Control specification
A+
B+
A-
B-
A
B
A input
B output

## Slide 30: Control specification
A+
B+
A-
B-
A
B

## Slide 31: Control specification
A+
B-
A-
B+
A
B

## Slide 32: Control specification
A+
C-
A-
C+
A
C
B+
B-
B
C

## Slide 33: Control specification
A+
C-
A-
C+
A
C
B+
B-
B
C

## Slide 34: Control specification
C
C
Ri
Ro
Ai
Ao
Ri+
Ao+
Ri-
Ao-
Ro+
Ai+
Ro-
Ai-
Ri
Ro
Ao
Ai
FIFO
cntrl

## Slide 35: A simple filter: specification
y := 0;
loop
x := READ (IN);
WRITE (OUT, (x+y)/2);
y := x;
end loop
Rin
Ain
Aout
Rout
IN
OUT
filter

## Slide 36: A simple filter: block diagram
x
y
+
control
Rin
Ain
Rout
Aout
Rx
Ax
Ry
Ay
Ra
Aa
IN
OUT
x and y are level-sensitive latches (transparent when R=1)
+ is a bundled-data adder (matched delay between Ra and Aa)
Rin indicates the validity of IN
After Ain+ the environment is allowed to change IN
(Rout,Aout) control a level-sensitive latch at the output

## Slide 37: A simple filter: control spec.
x
y
+
control
Rin
Ain
Rout
Aout
Rx
Ax
Ry
Ay
Ra
Aa
IN
OUT
Rin+
Ain+
Rin-
Ain-
Rx+
Ax+
Rx-
Ax-
Ry+
Ay+
Ry-
Ay-
Ra+
Aa+
Ra-
Aa-
Rout+
Aout+
Rout-
Aout-

## Slide 38: A simple filter: control impl.
Rin+
Ain+
Rin-
Ain-
Rx+
Ax+
Rx-
Ax-
Ry+
Ay+
Ry-
Ay-
Ra+
Aa+
Ra-
Aa-
Rout+
Aout+
Rout-
Aout-
C
Rin
Ain
Rx
Ax
Ry
Ay
Aa
Ra
Aout
Rout

## Slide 39: Control: observable behavior
Rx+
Rin+
Ax+
Ra+
Aa+
Rout+
Aout+
z+
Rout-
Aout-
Ry+
Ry-
Ay+
Rx-
Ax-
Ay-
Ain-
Ain+
Ra-
Rin-
Aa-
z-
C
Rin
Ain
Rx
Ax
Ry
Ay
Aa
Ra
Aout
Rout
z

## Slide 40: Taking delays into account
x+
x-
y+
y-
z+
z-
x
z
y
x’
z’
Delay assumptions:
  Environment: 3 times units
  Gates: 1 time unit
events: x+  x’-  y+  z+  z’-  x-  x’+  z-  z’+  y- 
time: 3 4 5 6 7 9 10 12 13 14

## Slide 41: Taking delays into account
x+
x-
y+
y-
z+
z-
x
z
y
x’
z’
Delay assumptions: unbounded delays
events: x+  x’-  y+  z+  x-  x’+  y-
time: 3 4 5 6 9 10 11
very slow
failure !

## Slide 42: Gate vs wire delay models
Gate delay model: delays in gates, no delays in wires
Wire delay model: delays in gates and wires

## Slide 43: Delay models for async. circuits
Bounded delays (BD): realistic for gates and wires.
  Technology mapping is easy, verification is difficult
Speed independent (SI): Unbounded (pessimistic) delays for gates and “negligible” (optimistic) delays for wires.
  Technology mapping is more difficult, verification is easy
Delay insensitive (DI): Unbounded (pessimistic) delays for gates and wires.
  DI class (built out of basic gates) is almost empty
Quasi-delay insensitive (QDI): Delay insensitive except for critical wire forks (isochronic forks).
  In practice it is the same as speed independent
BD
SI  QDI
DI

## Slide 44: Motivation (designer’s view)
Modularity for system-on-chip design
  Plug-and-play interconnectivity
Average-case peformance
  No worst-case delay synchronization
Many interfaces are asynchronous
  Buses, networks, ...

## Slide 45: Motivation (technology aspects)
Low power
  Automatic clock gating
Electromagnetic compatibility
  No peak currents around clock edges
Security
  No ‘electro-magnetic difference’ between logical ‘0’ and ‘1’in dual rail code
Robustness
  High immunity to technology and environment variations (temperature, power supply, ...)

## Slide 46: Dissuasion
Concurrent models for specification
  CSP, Petri nets, ...: no more FSMs
Difficult to design
  Hazards, synchronization
Complex timing analysis
  Difficult to estimate performance
Difficult to test
  No way to stop the clock

## Slide 47: But ... some successful stories
Philips
AMULET microprocessors
Sharp
Intel (RAPPID)
Start-up companies:
  Theseus logic, ADD Inc., Self-Timed Solutions
Recent blurb: It's Time for Clockless Chips, by Claire Tristram (MIT Technology Review, v. 104, no.8, October 2001: http://www.technologyreview.com/magazine/oct01/tristram.asp)
….