## Slide 1: Logic design of asynchronous circuits
Part IV:
Large
Asynchronous
Systems

## Slide 2: Why Asynchronous Logic?
Low Power
  Do nothing when there is nothing to be done
Modularity
  Added design freedom and component reusability
Electromagnetic Interference (EMI)
  Clocks concentrate noise energy at particular frequencies
Security?
  Surprise the hackers!

## Slide 3: Contents
Some asynchronous microprocessors
Problems in processor design
Problems and opportunities in asynchronous design
Example solutions to a selection of problems
Memories and peripherals
Design styles
GALS and asynchronous interconnection
Conclusions

## Slide 4: Why Microprocessors?
Well defined problem
  Easy to demonstrate correct function
Self-contained
  Make stand-alone devices
Not obviously suited to asynchronous techniques
  Forced to examine ‘real’ problems
Interesting problems
  New techniques to devise

## Slide 5: Microprocessors as Design Examples
AMULET1 (1994)
ARM6 compatible processor (almost)
1.0um 60 000 transistors
Hand designed
Bundled data, two-phase control
Feasibility study
Experiences
Two-phase logic hard to work with and interface to

## Slide 6: Microprocessors as Design Examples
AMULET2e (1996)
ARM7 compatible processor
Asynchronous cache
0.5um 450 000 transistors
Hand designed
Bundled data, four-phase control
Experiences:
Easy to use, self-contained system

## Slide 7: Microprocessors as Design Examples
AMULET3i (2000)
ARM9 compatible processor
SoC: Memory, DMA controller, bus, …
0.35um 800 000 transistors
Mostly hand designed
Bundled data, two-phase control
Commercial application (DRACO)
Experiences:
Universities don’t have the resources for such projects!

## Slide 8: Microprocessors as Design Examples
SPA (2002)
ARM10 compatible processor
0.18um well over 1 million transistors
Mostly synthesized
Dual-rail, four-phase control
Secure smartcard chip
Experiences:
To be confirmed
?

## Slide 9: Other Asynchronous Microprocessors
“Caltech Asynchronous Microprocessor” (1989)
  First asynchronous microprocessor
University of Tokyo’s “TITAC-2” (1997)
  Mostly hand designed
Caltech “MiniMIPS” (R3000) (1997)
  Hand designed

## Slide 10: Other Asynchronous Microprocessors
IMAG (Grenoble) “ASPRO-216” (1998)
  16-bit signal processor
Philips Research Laboratories 80C51 (1998)
  Synthesized using “Tangram” tool
Theseus Star-8 (2000)
  Uses Null Convention Logic (NCL)

## Slide 11: AMULET3 Processor Architecture
Highly pipelined structure
Similar to synchronous architecture
Features:
Branch prediction
Halting
Forwarding
Out-of-order completion
Precise exceptions

## Slide 12: Synchronous vs. Asynchronous Architectures
An AMULET looks very like a synchronous ARM
  Functional blocks divided by pipeline latches
But:
Some ideas can be ‘copied', some need reinvention
Some synchronous ‘tricks’ don’t work in an asynchronous environment
  Non-local interactions, dependency resolution, ...
Pipelining is too easy
  Temptation to inefficient design

## Slide 13: Data-dependent Timing
ARM instructions allow a shift before an ALU operation
These are rarely exploited
The shifter is often bypassed
The execution timing may be adjusted appropriately

## Slide 14: Process-level Parallelism
Example: decode and execute stages
Various threads – many invoked conditionally
Skewed pipeline latches (lower power EMI)
Variable stage delay (e.g. ‘stretch’ for series shift)
Differing pipeline depths (extra buffer for LDM/STM)
Conditional invocation of functions

## Slide 15: PC Pipeline
In a synchronous design non-local values can be read
The ARM uses the PC as an operand (e.g. relative branch)
The actual value is two instructions ‘out’ due to the pipeline depth of the original implementation

## Slide 16: PC Pipeline
In an asynchronous design only ‘adjacent’ stages can communicate
AMULET supplies the PC value with every instruction
This can be adjusted as required in an implementation independent manner

## Slide 17: Thumb Expansion
Handshaking allows pipeline occupancy to be changed without global control
Thumb instructions normally fetched in pairs but executed individually
Same scheme applied to (e.g.) ‘Load Multiple’
Similar scheme applied to removing ‘surplus’ packets

## Slide 18: Halting
Any unit can impose an arbitrary delay
A pipeline stage could choose to delay indefinitely
This will halt the whole pipeline shortly thereafter
  Downstream stages ‘drain’
  Upstream stages ‘back up’
Halted CMOS circuits use ‘no’ power
  No clock power either
Restart is instantaneous
Both AMULET2 and AMULET3 exploit this
for easy power management

## Slide 19: Colouring
Branches change the local colour and request a new stream
Prefetched operations discarded until a new stream arrives
Pipeline occupancy may be non-deterministic

## Slide 20: Deadlock
Question: if pipeline occupancy is variable, what happens if a token is inserted into a ‘full’ pipeline?
Answer: Deadlock!
a danger with the large number of states available
can be avoided with careful design
Two cases in AMULET3:
Branches when the prefetch pipeline is full
Memory conflict between instruction and data fetches
Both were known early and prevented at a higher level

## Slide 21: Data Aborts
Wait for MMU to abort or not
Stretch cycle if memory access

## Slide 22: Data Aborts
Speculate on memory not aborting
Register results returned out of order
More parallelism => higher throughput

## Slide 23: Reorder Buffer
Allows instructions to complete in any order
Resolves register dependencies
Allows register forwarding
Permits low-overhead memory management
Supports exact page fault exceptions

## Slide 24: Reorder Buffer
Data can arrive along any path at any time, providing their targets are mutually exclusive
Read out waits for each register to be filled in turn, then copies out the result (or not, if unwanted)
Copy out frees the register but does not delete the data

## Slide 25: AMULET3i Memory System
The RAM is ‘dual-port’ (at this level)
The instruction bus is simpler
  so it has a higher bandwidth

## Slide 26: Memory Structure
The local RAM is divided into 1 Kbyte blocks
Unified RAM model
Close to dual-port efficiency
About 50% instruction fetches are from the ‘Ibuffers’

## Slide 27: AMULET2e Cache
Pipelined
Data-dependent timing
Asynchronous line fetch
Newer design includes:
Copy-back
Write buffer
Victim cache

## Slide 28: Synthesis vs. Hand Design
Most of the AMULET3i system was designed at schematic level
Part (the DMA controller) was a test of Balsa
  A new asynchronous synthesis system
Synthesised blocks are more efficient to design but less efficient in operation
Suitable for (e.g.) peripherals that are rarely invoked
  No timing closure problems!

## Slide 29: DMAC
About 70 000 transistors
Regular structures (register banks) in full custom
Control synthesised from Balsa description
Cheats slightly by letting a clock into one corner!

## Slide 30: SPA
A project to produce a synthesisable ARM core in Balsa
Simple 3-stage pipelining
Omits many ‘performance’ features
Uses dual-rail coding to enhance security
Retargettable to any process, including dual-rail, 1-of-N codes etc. by recompilation

## Slide 31: AMULET3 vs. SPA

## Slide 32: Asynchronous on-chip Interconnection
MARBLE
Centrally arbitrated, multi-channel, asynchronous on-chip bus
Supports: 8-, 16- and 32-bit transfers, bus locking, sequential bursts, …
Separate, decoupled, asynchronous transfer phases for address and data
32-bit bundled data pathways
Used on AMULET3i
Standard ‘master’ and ‘slave’ interfaces
Standard interface to on-chip synchronous bus too

## Slide 33: Asynchronous on-chip Interconnection
CHAIN
Delay insensitive coding for ‘distance’ transmission
Requires more wires per bit
Exploit lack of clock to send serial symbols fast
4 wires, 2-bit (1-of-4) symbols
Point-to-point unidirectional wiring
Standard ‘master’ and ‘slave’ interfaces
Could easily provide standard synchronous interfaces

## Slide 34: GALS
Globally Asynchronous, Locally Synchronous interconnection
Use ‘conventional’ synchronous design blocks for SoC
Use asynchronous interconnection to avoid timing closure problems
May be the first big application of asynchronous logic
No reason why the ‘local’ blocks need to be synchronous …

## Slide 35: AMULET3i
AMULET3 microprocessor (ARMv4T)
8 Kbytes RAM
16 Kbytes ROM
Flexible, multi-channel DMAC
Programmable memory interface
On-chip asynchronous bus (MARBLE)
Bridge to on-chip synchronous bus
Configuration registers
Software debug support
Test interface

## Slide 36: Experience of Large Asynchronous Designs
Hard, but feasible
Competitive
Advantages?
  Power management
  EMI
  Composability (GALS)
  Security?
Commercial
  Philips, Theseus, ADD, Intel?, …

## Slide 37: Conclusions
Asynchronous logic:
Can be competitive with ‘conventional’ designs
Has advantages with low-power and low EMI
  think portable systems
May be the only solution for some tasks
  block interconnections on large chips
but
Designing big systems is a lot of work
It’s hard to catch up with the big companies